## Slide 1: SystemC Investigation

## Slide 2: Table of Contents
SystemC Definition
Verilog: always vs. SystemC: thread
SystemC: thread
Modules
Port and Data Type
Process
Method Process vs Thread Process
Sentivity List
Constructor
Operation

## Slide 3: Table of Contents
Introduction to High-level design
System-level design
High-level design
Problem of RTL Design Flow
Solution with High-level Design Flow
Comparison between RTL and HLD
Aims of High-level Design
High-level Design Flow: Design step and EDA tool

## Slide 4: SystemC Definition
SystemC is a set of C++ class that realize hardware description and simulation
SystemC follows the C++'s syntax.
We can run its simulation using general C++ compiler.
We can run its simulation together with Verilog design, using VCS/NC simulator

## Slide 5: Verilog: always vs. SystemC: thread

## Slide 6: SystemC: thread

## Slide 7: Modules
A Module is the basic structural building block in SystemC. It is a container class in which processes and other modules are instantiated
Format
  SC_MODULE( name ) {
  sc_in input_port; // (1) Port and data type
  sc_out output_port;
  function() { // (2) Process, contrstructor and operation
  task;
  }
  };

## Slide 8: Port and Data Type
Port:
  sc_in < data_type > input_nm;
  sc_out < data_type > input_nm;
Data type:
  <bool> : 1-bit
  sc_uint<N> : N-bit unsigned
  sc_int<N> : N-bit signed
  sc_bigunit
  sc_biginit

## Slide 9: Process
Functions executed in parallel.
Purpose: to describe structure of a circuit
  void func_name(void){
  reset task
  wait();
  while(1){
  normal task
  wait();
  }
  }

## Slide 10: Method Process vs Thread Process
Method | Thread
The entire body of the method process is executed. After completed, returns control to SystemC kernel. All local variables lose their value. Faster than thread processes | Executes until wait(). After executed wait(), process suspends and is saved its state. The process is resumed based upon its sensitivity list. Can be used to model: state machine, . . .

## Slide 11: Sentivity List
Processes have sensitivity lists, i.e. a list of signals that cause the process to be invoked.
2 types:
  Dynamic sensitivity list
  Static sensitivity list

## Slide 12: Constructor
A special function.
Purpose: to specify functions need to be treated as process.
  SC_CTOR( name ) {
  SC_CTHREAD( proc0 , clk.pos() );
  reset_signal_is( reset , true );
  }

## Slide 13: Operation
A function to do specific operation.
Purpose: to describe operations.

## Slide 14: Introduction to High-level design
Electronic machineries are getting more and more complicated, higher and higher performance and necessary to improve the design productivity.
Design methodology changed drastically in every ten years. Now, it's time to shift to system/behavior level

## Slide 15: System-level design
Develop appropriate hardware and software specifications according to system specification
Purpose: Make HW/SW design very efficient and reduce total development period and cost

## Slide 16: High-level design
Design HW at higher level (i.e behavioral) in SystemC. RTL description (Verilog HDL) is synthesized by a tool from the SystemC description
Purpose: Reduce HW design cost by designing at abstract level

## Slide 17: Problem of RTL Design Flow
Number of lines of design description increases as LSIs get larger and more complicated
Simulation speed becomes slower
Difficult to verify, debug, modify or maintain the large design

## Slide 18: Solution with High-level Design Flow
Design HW at a higher level of abstraction
Use SystemC as a high level design language and reduce number of lines of design description
Incorporate new behavioral synthesis technology and reduce man effort to design in detail

## Slide 19: Comparison between RTL and HLD

## Slide 20: Aims of High-level Design
Efficient design at a higher abstraction level
  Design size (i.e. Number of lines of design description) can be reduced to one third of RTL (in Verilog)
  => Number of design errors is reduced
  => Easy to correct design errors
  IPs become more flexible at an abstraction level so that they can be reused more efficiently
  => Reduce total design effort by using such proven designs
Optimize HW architecture in short period of time

## Slide 21: High-level Design Flow: Design step and EDA tool

## Slide 22: The End Thanks for listening