## Slide 1: Video IP Investigation
Renesas Design Vietnam Co., Ltd.
Tu Tran, VideoIP

## Slide 2: Table of Contents
Definitions
Capturing Video
Spatial Sampling
Temporal Sampling
Frames and Fields
Color Spaces
RBG
YCbCr (YUV)

## Slide 3: Table of Contents
The Relation between RBG and YUV
YCbCr Sampling Formats
Video Coding Concepts
Video Codec
  Video Encoder
  Video Decoder
Temporal Model
  Block-based Motion Estimation and Compensation
  Macroblock & Block Size

## Slide 4: Table of Contents
Spatial Model
  Transform Coding
  The Discrete Cosine Transform (DCT)
  Quantisation
  Reordering and Zero Encoding
  Entropy Encoding
    Predictive Coding
    Variable-length Coding
    Arithmetic Coding
      Arithmetic Encoding Example
      Arithmetic Decoding Example

## Slide 5: Table of Contents
H.264/MPEG4 Part 10
  Intra Prediction
    4 × 4 Luma Prediction Modes
    16 × 16 Luma Prediction Modes
    8 × 8 Chroma Prediction Modes
  Inter Prediction
    Tree structured motion compensation
    Motion Vectors & Motion Vector Prediction
    Luma Interpolation Process (half-pel samples)
    Luma Interpolation Process (quarter-pel samples)
    Chroma Interpolation Process (eighth-sample positions)
  Deblocking Filter

## Slide 6: Definitions
Pixel is a picture element.
Resolution is the number of elements in a picture or frame. For example
  TV: 640x480
  HD: 1280x720
  Full HD 1920x1080
Frame is picture that is formed by many pixels
Video is a sequence of frames and captured by using progressive or interlaced sampling .

## Slide 7: Capturing Video
Digital video is a representation of a natural (real-world) visual scene, sampled spatially and temporally
Each spatio-temporal sample (picture element or pixel) is represented as a number or set of numbers that describes the brightness (luminance) and color of the sample.

## Slide 8: Spatial Sampling
The most common format for a sampled image is a rectangle with the sampling points positioned on a square or rectangular grid
Sampling occurs at each of the intersection points on the grid and the sampled image may be reconstructed by representing each sample as a square picture element (pixel).
The visual quality of the image is influenced by the number of sampling points.

## Slide 9: Spatial Sampling

## Slide 10: Temporal Sampling
A moving video image is captured by taking a picture at periodic time intervals
A higher temporal sampling rate (frame rate) gives apparently smoother motion in the video scene but requires more samples to be captured and stored.
A video signal may be sampled as a series of complete frames (progressive sampling) or as a sequence of interlaced fields (interlaced) sampling

## Slide 11: Frames and Fields
An interlaced video sequence contains a series of fields and half of the data in a frame (one field) is sampled at each temporal sampling interval.
A field consists of either the odd-numbered or even-numbered lines
Send twice as many fields per second as the number of frames

## Slide 12: Frames and Fields
Top field
Bottom field
A frame

## Slide 13: Color Spaces
Video needs a mechanism to capture and represent color information
Color images require at least three numbers per pixel position to represent color accurately.
The method chosen to represent brightness (luminance or luma) and color is described as a color space.
2 types: RBG, YCbCr

## Slide 14: RBG
In the RGB colour space, a colour image sample is represented with three numbers Red, Green and Blue
Any colour can be created by combining red, green and blue in varying proportions
From a normal viewing distance, the separate components merge to give the appearance of ‘true’ colour.

## Slide 15: YCbCr (YUV)
Because of the human visual system (HVS), represent a color image more efficiently by separating the luminance from the color information and representing luma with a higher resolution than color.
Y is the luminance component and Cb, Cr are color difference (chrominance or chroma) components of blue and red

## Slide 16: The Relation between RBG and YUV

## Slide 17: YCbCr Sampling Formats
4:4:4 sampling: chrominance components have same resolution as luminance component

## Slide 18: YCbCr Sampling Formats
4:2:2 sampling (YUY2): chrominance components have half the horizontal resolution of luminance component

## Slide 19: YCbCr Sampling Formats
4:2:0 sampling (YV12): chrominance components have half the horizontal and vertical resolution of luminance component

## Slide 20: Video Coding Concepts
Video compression (video coding) is the process of compacting or condensing a video into a smaller number of bits.
Uncompressed video typically requires a large bitrate and compression is necessary for practical storage and transmission of digital video.
Compression involves a complementary pair of systems, a compressor (encoder) and a decompressor (decoder).

## Slide 21: Video Coding Concepts
Data compression is achieved by removing redundancy, i.e. components that are not necessary
Methods: temporal and spatial redundancy

## Slide 22: Video Codec
Encodes a source image or video sequence into a compressed form and decodes this to produce a copy (lossless) or approximation (lossy) of the source sequence
Consists of three main functional units: a temporal model, a spatial model and an entropy encoder.

## Slide 23: Video Encoder

## Slide 24: Video Decoder

## Slide 25: Temporal Model
Purpose: reduce redundancy between transmitted frames
Input: uncompressed video (frames)
Output: residual frames and motion vectors
A practical and widely-used method is Block-based Motion Estimation and Compensation

## Slide 26: Block-based Motion Estimation and Compensation
Compensate for movement of rectangular sections or ‘blocks’ of the current frame
Procedure:
  Search an area in the reference frame to find the best match (motion estimation)
  The chosen region is subtracted from the current block to form a residual M × N block (motion compensation)
  The residual block and the offset between the current block and the position of the candidate region (motion vector) are encoded and transmitted

## Slide 27: Macroblock & Block Size
The macroblock, corresponding to a 16×16-pixel region of a frame, is the basic unit for motion compensated prediction in a number of important visual coding standards
Block Size smaller motion compensation block sizes can produce better motion compensation results.
However, a smaller block size leads to increased complexity (more search operations must be carried out) and an increase in the number of motion vectors that need to be transmitted.

## Slide 28: Spatial Model
Purpose: decorrelate image or residual data further and to convert it into a form that can be efficiently compressed using an entropy coder
Input: residual frames
Output: quantised transform coefficients
Three main components, transformation (decorrelates and compacts the data), quantisation (reduces the precision of the transformed data) and reordering (arranges the data to group together significant values).

## Slide 29: Transform Coding
Convert image or motion-compensated residual data into another domain (the transform domain).
Popular transforms: Discrete Cosine Transform (DCT), Discrete Wavelet Transform (DWT or just ‘wavelet’) . . .

## Slide 30: The Discrete Cosine Transform (DCT)
Y = AXAT
Where X is a matrix of samples, Y is a matrix of coefficients and A is an N × N transform matrix. The elements of A are:
These coefficients can be considered as ‘weights’ of a set of standard basic patterns. Any image block may be reconstructed by combining all N × N basis patterns

## Slide 31: Quantisation
A quantiser maps a signal with a range of values X to a quantised signal with a reduced range of values Y (reduce bit length).
Where QP is step size
Quantization is not reversible
If the step size is large, the range of quantised values is small and can therefore be highly compressed and and vice versa

## Slide 32: Reordering and Zero Encoding
Scan
Raster scan
Z-scan

## Slide 33: Reordering and Zero Encoding
Run-level encode
  (run, level) pairs where run indicates the number of zeros preceding a nonzero coefficient and level indicates the magnitude of the nonzero coefficient.
  Example:
Input array: 16,0,0,−3,5,6,0,0,0,0,−7, . . .
Output values: (0,16),(2,−3),(0,5),(0,6),(4,−7). . .

## Slide 34: Entropy Encoding
Purpose: converts symbols into a compressed bitstream suitable for transmission or storage
Input: quantised transform coefficients, motion vectors, . . .
Output: bitstream
Encoding method: Predictive Coding, Variable-length Coding, Arithmetic Coding

## Slide 35: Predictive Coding
Predicting elements of the current block or macroblock from previously-encoded data and encoding the difference between the prediction and the actual value
B
C
A
X
Motion vector X is predicted from Vectors A, B and C

## Slide 36: Variable-length Coding
Maps input symbols to a series of codewords (variable length codes or VLCs).
Less common symbols are represented with long VLCs and vice versa
Method: Huffman Coding
Vector Probability(p) log2(1/p)‏
-2 0.1 3.32
-1 0.2 2.32
0 0.4 1.32
1 0.2 2.32
2 0.1 3.32
p=0.1
p=0.1
p=0.2
p=0.2
C
A
-2
2
B
-1
1
D
p=0.4
0
p=0.4
p=0.2
p=0.6
p=1.0
1
0
1
0
1
0
0
1
Codeword of vector 2: 001

## Slide 37: Arithmetic Coding
Converts data symbols into a single fractional number
Optimize fractional number of bits required to represent each symbol
Ex:
Vector Probability(p) log2(1/p) sub-range
-2 0.1 3.32 0.0-0.1
-1 0.2 2.32 0.1-0.3
0 0.4 1.32 0.3-0.7
1 0.2 2.32 0.7-0.9
2 0.1 3.32 0.9-1.0

## Slide 38: Arithmetic Encoding Example
Sequence data (0, -1, 0, 2)‏
0 0.1 0.3 0.7 0.9 1.0
(-2) (-1) (0) (1) (2)‏
(-1)
0.3
0.34
0.42
0.7
(0)
0.396
0.364
0.42
(2)
0.3928
0.396
Transmitted number is 0.394

## Slide 39: Arithmetic Decoding Example
==>The decoded data (0, -1, 0, 2)‏
0 0.1 0.3 0.7 0.9 1.0
(-2) (-1) (0) (1) (2)‏
(-1)
0.3
0.34
0.42
0.7
(0)
0.34
0.396
0.364
0.42
0.364
0.3928
(-2) `

## Slide 40: H.264/MPEG4 Part 10

## Slide 41: Intra Prediction
a prediction block P is formed based on previously encoded and reconstructed blocks and is subtracted from the current block prior to encoding
form for each 4 × 4 block or for a 16 × 16 macroblock
9 optional prediction modes for each 4 × 4 luma block, 4 modes for a 16 × 16 luma block and 4 modes for the chroma components.
selects the prediction mode for each block that minimises the difference between P (prediction block) and the block to be encoded

## Slide 42: 4 × 4 Luma Prediction Modes Intra Prediction

## Slide 43: 16 × 16 Luma Prediction Modes Intra Prediction
Mode 0 (vertical) Extrapolation from upper samples (H)
Mode 1 (horizontal) Extrapolation from left samples (V)
Mode 2 (DC) Mean of upper and left-hand samples (H + V).
Mode 4 (Plane) A linear ‘plane’ function is fitted to the upper and left-hand samples H and V

## Slide 44: 8 × 8 Chroma Prediction Modes Intra Prediction
are very similar to the 16×16 luma prediction modes
except that the numbering of the modes is different. The modes are DC(mode 0), horizontal (mode 1), vertical (mode 2) and plane (mode 3).

## Slide 45: Inter Prediction
creates a prediction model from one or more previously encoded video frames or fields using block-based motion compensation
support for a range of block sizes (from 16 × 16 down to 4×4) and fine subsample motion vectors (quarter-sample resolution in the luma component)

## Slide 46: Tree structured motion compensation Inter Prediction
The luminance component of each macroblock (16×16 samples) may be split up in four ways
If the 8×8 mode is chosen, each of the four 8×8 sub-macroblocks within the macroblock may be split in a further 4 ways

## Slide 47: Motion Vectors & Motion Vector Prediction Inter Prediction
Each partition or sub-macroblock partition in an inter-coded macroblock is predicted from an area of the same size in a reference picture
The offset between the two areas (the motion vector) has quarter-sample resolution for the luma component and one-eighth-sample resolution for the chroma components.
Encoding a motion vector can cost a significant number of bits, especially if small partition sizes are chosen
Motion vectors for neighbouring partitions are often highly correlated. A predicted vector, MVp, is formed based on previously calculated motion vectors

## Slide 48: Luma Interpolation Process (half-pel samples)
Interpolated from integer-position samples using a six tap Finite Impulse Response (FIR) filter with weights (1/32,−5/32, 5/8, 5/8,−5/32, 1/32)
For example, half-pel sample b is calculated from the six horizontal integer samples E, F, G, H, I and J:
b = round((E − 5F + 20G + 20H − 5I + J) /32)
Interpolation of luma half-pel positions

## Slide 49: Luma Interpolation Process (quarter-pel samples)
Quarter-pel samples are produced after all the half-pel samples are available
Quarter-pel positions with two horizontally or vertically adjacent half- or integer-position samples are linearly interpolated between these adjacent samples, for example: a = round((G + b) / 2)
The remaining quarter-pel positions (e, g, p and r in the figure) are linearly interpolated between a pair of diagonally opposite half -pel samples. For example, e is interpolated between b and h.
Interpolation of luma quarter-pel positions

## Slide 50: Chroma Interpolation Process (eighth-sample positions)
generated at eighth-sample intervals between integer samples in each chroma component using linear interpolation
Ex: a = round([(8 − dx ) · (8 − dy)A + dx · (8 − dy)B + (8 − dx ) · dyC + dx · dyD]/64)
Interpolation of chroma eighth-sample positions

## Slide 51: Deblocking Filter
A filter is applied to each decoded macroblock to reduce blocking distortion
Applied after the inverse transform in the encoder and before reconstructing and displaying the macroblock in the decoder
The filter smooths block edges, improving the appearance of decoded frames

## Slide 52: Deblocking Filter
Filtering is applied to vertical or horizontal edges of 4×4 blocks in a macroblock in the following order:
    1. Filter 4 vertical boundaries of the luma component (in order a, b, c, d in Figure 6.29).
    2. Filter 4 horizontal boundaries of the luma component (in order e, f, g, h, Figure 6.29).
    3. Filter 2 vertical boundaries of each chroma component (i, j).
    4. Filter 2 horizontal boundaries of each chroma component (k, l).

## Slide 53: The End Thanks for listening

## Slide 54: Confirm the action items
AI#1: fix slide 5 picture about pixels.
=> Correct information: slide 6
AI#2: slide 8 add, fix the example about field
=> Correct information: slide 9
AI#3: add investigation about prediction process (6.4.5 - 6.4.6)
=> Correct information: slide 41, 45
AI#4: add deblocking filter information (6.4.7)
=> Correct information: slide 51